## Slide 1
Department of ECE
College of Engineering Guindy, Anna University, Chennai
Intelligent Battery Health Monitoring
and Predictive Management
Project Members:
Madhavshankar K (Reg. No.: 2023105023)
Ragul S (Reg. No.: 2023105041)
Akash Rajan R (Reg. No.: 2023105508)
EC23702 – MINI PROJECT
Review I
07/08/2026
Under the Guidance of:
Dr K Praveen
Assistant Professor (SI. Gr.)
Department of ECE
CEG Campus, Anna University

## Slide 2
Introduction
Literature Review
Problem Statement
Objectives
Proposed Methodology
Results
Timeline
References
Layout

## Slide 3
Modern EVs rely on Li-ion battery packs that need continuous monitoring of voltage, current, and temperature to stay safe and efficient.
Commercial low cost BMS units only perform voltage/current monitoring, basic balancing, and overcharge/over-discharge protection.
These systems are reactive, they respond only after a fault (overheating, weak cell, leakage) has already occurred.
This project aims to make the BMS intelligent and predictive estimating SOC/SOH, predicting thermal rise and weak cells, and optimizing charging/cooling before problems occur.
Scope: sensing → filtering → state estimation → predictive fault diagnosis → adaptive control (cooling, balancing, charging) → cloud/mobile reporting.
Introduction

## Slide 4
Paper Title | Methodology | Inference
“Passive and Active Battery Balancing Comparison Based on MATLAB Simulation” - Daowd, Omar, Van Den Bossche, Van Mierlo (Vrije Universiteit Brussel) | Simulink comparison of passive (resistor-bleed) vs. active (charge-transfer) cell balancing circuits under simulated charge/discharge cycles. | Active balancing gives faster convergence and higher energy efficiency than passive balancing; passive is simpler but wastes energy as heat — guided our choice of adaptive active balancing.
“Improved BMS: A Smart Electric Vehicle Design Based on an Intelligent Battery Management System” - Bhuvaneswari et al., ICICT 2024 (IEEE) | Smart BMS architecture combining real-time sensing with intelligent control logic for improved monitoring and protection in EVs. | Confirms the shift from threshold-based protection to intelligent, sensor-fused decision-making as the key novelty gap in low-cost EV BMS.
“Hierarchical Energy Optimization Strategy and Its Integrated Reliable Battery Fault Management for Hybrid Hydraulic Electric Vehicle” - Kamal & Adouane | Hierarchical control strategy layering energy optimization with fault management for reliability in hybrid electric-hydraulic vehicles. | Supports a layered architecture (estimation → fault prediction → control) and reinforces the need for integrated fault management, not just isolated protection triggers.
Literature Review

## Slide 5
Existing low-cost EV BMS units only do voltage/current monitoring, basic balancing, and overcharge/over-discharge protection, they cannot predict failure before it happens.
P1 - Cell leakage is detected only after severe degradation; the owner is warned too
late.
P2 - Noisy sensor signals cause false SOC, temperature, and balancing readings.
P3 - Cooling systems run on fixed thresholds, wasting energy.
P4 - Battery aging is ignored during charging, every cell is charged identically.
P5 - No predictive maintenance, the owner has no idea which cell is weakening or
when replacement is needed.
P6 - Most student BMS projects skip thermal-runaway prevention, adaptive cooling,
and health/fault prediction entirely.
Problem Statement

## Slide 6
01
Increase overall battery life
02
Prevent thermal runaway / explosion
03
Reduce energy loss in balancing
04
Detect weak cells early
05
Detect internal leakage
06
Optimize charging strategy
07
Enable adaptive cooling control
08
Improve overall system efficiency
09
Predict battery replacement need
Objectives

## Slide 7
Battery Pack (Voltage / Current / Temp Sensors)
Adaptive EKF Filtering
SOC / SOH Estimation
Leakage & Weak-Cell Detection
Predictive Thermal Model
(Temp-rise forecast)
Adaptive Cooling & Charging Control
ML Fault Prediction
Cloud DB + Mobile App Notification
Proposed Methodology

## Slide 8
Simulink model of the Li-ion cell built and validated and electrical behavior replicated ideally in simulation.
Real-time hardware tests conducted: charge/discharge cycling of 2500 mAh Li-ion cells with a 12 V DC motor of 200 RPM as load.
Current Status & Results
SOC VS TIME PLOT
Lookup (LU) table generated from the test data, now being fed into Simulink to drive a real-time-matched simulation.
TERMINAL VOLTAGE VS TIME PLOT

## Slide 9
Current Status & Results

## Slide 10
Ph 1-2
Battery fundamental + literature survey
Done
Ph 3
Simulink battery model (ideal)
Done
Ph 4
Conduction of charge/
discharge tests + LU table
Done
Ph 5
ML fault prediction models (temp/circuit/balancing)
Done
Ph 6
Integrate ML model into Simulink
In Progress
Ph 7
Coolant + balancing circuit design
Future
Ph 8
Full-system testing
Future
Currently at Phase 6 -- real-time Simulink integration of the ML fault-prediction model.
Timeline

## Slide 11
[1] M. Daowd, N. Omar, P. Van Den Bossche, and J. Van Mierlo, "Passive and Active Battery Balancing Comparison Based on MATLAB Simulation," Vrije Universiteit Brussel & Erasmus University College Brussels, Belgium.
[2] S. Bhuvaneswari, "Improved BMS: A Smart Electric Vehicle Design based on an Intelligent Battery Management System," 2024 International Conference on Inventive Computation Technologies (ICICT), IEEE, DOI: 10.1109/ICICT60155.2024.10544810.
[3] E. Kamal and L. Adouane, "Hierarchical Energy Optimization Strategy and Its Integrated Reliable Battery Fault Management for Hybrid Hydraulic-Electric Vehicle."
References